## Slide 1: Hackathon 102: RIFT
Things went much further and much better than expected !

## Slide 2: Participants
Writing Code
  Bruno R. /FREE RADICAL
  Don F. /HP
  Pascal T. /CISCO
  Ilya V./Mellanox
  TONY P. /JUNIPEr
  Here for the cookies and company
    JeFF T. /ALU
    Jeffrey Z. /Juniper
    Dima A. /YANDEX

## Slide 3: What is rift
RIFT: A NEW specialized protocol for IP fabrics, especially Datacenter
Mixture of link-state and distance vector protocol
Schema based

## Slide 4: Hackathon scope
Building a python implementation of initial discovery, adjacency state machine
Interoperability test between a public vendor package with the python implementation
More?
core_1> show interface if_1_202
Interface:
+-------------------------------------+-----------------+
| Interface Name | if_1_202 |
| Advertised Name | core_1-if_1_202 |
| Interface IPv4 Address | |
| Metric | 1 |
| Receive LIE IPv4 Multicast Address | 224.0.100.1 |
| Transmit LIE IPv4 Multicast Address | 224.0.100.2 |
| Receive LIE IPv6 Multicast Address | FF02::0078 |
| Transmit LIE IPv6 Multicast Address | FF02::0078 |
| Receive LIE Port | 20022 |
| Transmit LIE Port | 20021 |
| Receive TIE Port | 20023 |
| System ID | 1 |
| Local ID | 1 |
| MTU | 1500 |
| POD | 0 |
| State | THREE_WAY |
| Neighbor | Yes |
+-------------------------------------+-----------------+
Neighbor:
+----------------------------------+----------------+
| Name | None |
| System ID | 202 |
| IPv4 Address | 172.29.104.205 |
| LIE UDP Source Port | 20022 |
| Link ID | 28672 |
| Level | 1 |
| Flood UDP Port | 20024 |
| MTU | 1400 |
| POD | 0 |
| Hold Time | 3 |
| Not a ZTP Offer | False |
| You Are Not a ZTP Flood Repeater | False |
| Your System ID | 1 |
| Your Local ID | 1 |
+----------------------------------+----------------+

## Slide 5: First results
Three way adjacency came up within 3 hours
  Only problem found was multicast joins on different kernel picked interfaces
  Largely due to work done by Bruno R. upfront
Model based packet encoding removes 80+% bugs and work from normal protocol implementation work
Hence we ran out of initial scope quickly

## Slide 6: More results
Zero touch provisioning finite state machine
  ZTP finite state machine deciding at which level the node joins the fabric
  Large part of the code written
Large number of comments on the models, finite state machines and draft procedures