## Slide 1
IETF Hackathon: SPIN
IETF 102
14-15 July, 2018
Montreal

## Slide 2
Hackathon Plan
Roundtrip time measurement of encrypted transport flows
  draft-quic-*
  Heuristics based approach for more robust measurements with single bit.
Making the middlebox code more viable.
<number>

## Slide 3
What got done
Middlebox tracks multiple connections in parallel,
Middlebox uses heuristics to reject bad RTT samples.
A sequence of Netem links to introduce delay and reordering.
  Network impairments have substantially different effects on the spin bit observer depending on where on path they occur.
  The reduced sample frequency of spin bit observer does not not effect the estimated RTT substantially
<number>

## Slide 4
Example 5% reordering with depth of 10ms
Chart: 
| Median | 95th | 75th | 25th | 5th
Server Full | 32958 | 40975 | 35731 | 31010 | 23878.2
Server low | 33898 | 42004 | 36810 | 31606 | 24810.5
Spin | 35774.5 | 43820.75 | 38542.5 | 32287.75 | 25187.25

## Slide 5
What we learned
SPIN bit rocks!
<number>

## Slide 6
Wrap Up
Team members:
Marcus Ihlar
Al Morton
Emile Stephan
Roni Even
<number>